## Slide 1: Time and Frequency Domains z-transform

## Slide 2: Why introduce the z-transform?
The design and analysis of digital filters is aided by an understanding of the z-transform.

## Slide 3: What is the z-transform?
The z-transform is the discrete-time equivalent of the Laplace transform.
The Laplace transform is a generalisation of the continuous-time Fourier transform.
The z-transform is a generalisation of the discrete-time Fourier transform.
Notes: Familiarity, on the part of the students, with continuous-time linear signals and systems theory and the Laplace transform is assumed.
While a recurrent theme in this course is the representation of signals and systems in both time and frequency domains and great emphasis is given to the transformation, or mapping, between those two domains using Fourier analysis, the introduction of the z-transform completes the picture (so to speak) of discrete- as well as continuous-time linear time-invariant systems.
Discrete-time filters (systems) are very often described in terms of z-transfer functions.
We will see how these relate to alternative descriptions of discrete-time filters using difference equations or impulse responses.
The point made in this slide is that both Laplace and z-transforms are linked to Fourier analysis.

## Slide 4: Uses of the Laplace transform
Solution of continuous-time, linear differential equations
Representation of continuous-time, linear time invariant systems as s-transfer functions
Complex variable s may be viewed as an operator, representing differentiation with respect to time
Notes: As mentioned previously, some familiarity with continuous-time linear time-invariant system theory is assumed. The contents of this slide are a concise review of the use of Laplace transforms in that context.

## Slide 5: Uses of the z-transform
Solution of discrete-time, linear difference equations
Representation of discrete-time, linear time invariant systems as z-transfer functions
Complex variable z may be viewed as an operator representing a shift of one sample in a sequence
Notes: Here, a parallel is made between the application of the Laplace transform to continuous-time LTIs and the application of the z-transform to discrete-time LTIs.

## Slide 6: Definition of the z-transform
X(z) is a continuous function of complex variable z.
x(n) is a discrete-time sequence. It is a signal but, if considered to be an impulse response, it may represent, or characterise, a system.
Notes: This definition is the most general definition of the z-transform, sometimes referred to as the two-sided or bilateral z-transform (the summation limits are +/- infinity).
The z-transform of a discrete sequence x(n) is a polynomial expression in the complex variable z containing as many terms as the discrete sequence x(n).
In the context of digital signal processing, the discrete sequence x(n) will often represent a discrete-time sequence where n is interchangeable with t=nT.
The sequence x(n) may therefore be viewed as a discrete-time signal.
We will shortly see how the z-transform may be applied and interpreted if that discrete-time signal x(n) is considered to be the impulse response h(n) of a discrete-time system (and therefore characterises or represents a system).
In the context of ‘real-world’, physically realisable, systems, impulse response h(n) is likely to be right-sided (causal) and hence the use of a corresponding one-sided, or unilateral, z-transform (summation limits zero to infinity) is widespread.
We’ll see this in the following simple examples of deriving algebraic expressions for the z-transforms of different sequences.

## Slide 7: z-transform and Fourier transform
The z-transform is concerned with discrete-time signals (sequences).
The corresponding form of Fourier analysis is the discrete-time Fourier transform (DTFT).
The DTFT is defined as:
Notes: As stated earlier, the z-transform is a generalisation of the discrete-time Fourier transform. The expressions defining the z-transform and the DTFT are very similar.

## Slide 8: z-transform and DTFT
Expressing complex variable z in polar form, i.e.
The z-transform of x(n) is equivalent to the DTFT of x(n)r-n.
If r = 1 then the z-transform of x(n) is equivalent to the DTFT of x(n).
Recall that |z| = r.
Notes: Looked at from another perspective, the DTFT is a special case of the z-transform. It applies when the magnitude of the complex variable z is equal to one.

## Slide 9: z-transform of an exponential function
From the definition of the z-transform
Comparing this with the Taylor series approximation
for
We can write
for
There is a range of values of z , a region of convergence, for which X(z) is absolutely summable, i.e.
Notes: In most, if not all, textbook treatments of the z-transform, this is the first example presented.
Multiplying the exponential sequence by the unit step function u(n) creates a right-sided, causal sequence and may be represented by changing the summation limits from +/- infinity to zero to infinity.
The resultant summation is of the same form as that appearing in the Taylor series expression on the left hand side .
Consequently we can substitute a/z for p in the right hand side of the Taylor series expression.
It’s important to note that the Taylor series expression is true only for p, or (a/z), less than 1.
In creating a simple algebraic expression, rather than an infinite series of terms in decreasing powers of z, we have had to introduce a condition on (the magnitude of) z.

## Slide 10: z-transform of an exponential function
From the definition of the z-transform
Letting
for
Notes: At first sight you might wonder about the significance of this apparently esoteric sequence.
Don’t worry about that for now.
Just follow the derivation(of its z-transform) and then observe that the resulting expression for x(z) is identical to that in the previous example.
However, the constraint on the values of z for which it holds is different.

## Slide 11: z-transform of an exponential function
for
Two different sequences have exactly the same algebraic expression for their z-transform.
The algebraic expression for a z-transform alone does not specify a unique sequence. The condition part of the z-transform must be taken into account.
The conditions on the values of z define regions of convergence (ROCs)
for
Notes: The region of convergence is an integral part of a z-transform (the representation of a sequence in the z-domain) and good tables of z-transforms should include these.
Regions of convergence have some interesting and useful (in terms of our being able to inverse transform) properties. These are tied up intimately with two more things – poles and zeros (of a z-transform) and the relationship between the z-transform and the (discrete-time) Fourier transform
We’ll describe these two next – apologies for seeming to introduce more and more arbitrary concepts. They will all be tied together shortly.

## Slide 12: Poles and zeros of a z-transform
The poles of a z-transform are the values of z for which
The zeros of a z-transform are the values of z for which
For rational X(z), i.e. when X(z) is a ratio of polynomials in z, you can find/plot poles and zeros.
Notes: Students are assumed to be familiar with the concept of poles and zeros applied to continuous-time LTIs.

## Slide 13: Regions of convergence
A region of convergence (ROC) specifies the values of the complex variable z for which |X(z)| < ∞.
Its graphical interpretation is as an area in the (complex) z-plane.
Notes: We mentioned ROCs a few slides back. The first point on this slide summarises the definition of a ROC.
The values of the complex variable z (that make up the ROC) might be plotted in the z-plane. In the next few slides we will see that these values make up an area or region of the z-plane with simple geometrical properties.

## Slide 14: ROC properties
The ROC of X(z) does not contain any poles of X(z).
ROC boundaries depend on |z| and hence are circles in the z-plane (centred on the origin).
A ROC is a single connected region in the z-plane.
If x(n) is finite then the ROC is the entire z-plane except, possibly, for 0 or infinity.
Stable systems (for which a discrete-time Fourier transform exists) have ROCs that contain the unit circle.
Notes: Poles of x(z) are values of z for which X(z) equals, or tends to, infinity.
ROC describes values of z for which |X(z)| is less than infinity. Hence poles and ROCs are incompatible.
Recall the two (exponential function) examples given earlier. The Taylor series simplifications of X(z) were contingent upon the value of |z|.
The DTFT is a special case of the z-transform when |z| is equal to one, i.e. the unit circle in the z-plane. Frequency domain considerations apply to stable systems.

## Slide 15: ROC properties
If x(n) is right-sided then the ROC extends outwards from a circle containing the outermost pole of X(z).
Notes: Consider a system having two poles as shown in this diagram. Three different ROCs satisfy, or possess, the aforementioned properties. We could turn the statements on these three slides on their heads and state, for example, that if we consider a ROC that extends outwards from a circle containing the outermost pole of X(z) then the corresponding x(n) will be right-sided. Causal systems have right-sided impulse responses...

## Slide 16: ROC properties
If x(n) is left-sided then the ROC is inside a circle that does not contain the innermost pole of X(z).
Re
Im
z
-plane
ROC
Notes: As stated earlier, the same X(z) with the same poles and zeros may be associated with more than one valid region of convergence. If we consider a ROC that extends inwards from a circle inside the innermost pole of X(z) then the corresponding x(n) will be left-sided, i.e. non-causal.

## Slide 17: ROC properties
If x(n) is two-sided then the ROC is a ring bounded by circles inside the outermost pole of X(z) and outside the innermost pole of X(z).
ROC
Re
Im
z-plane
Notes: If we consider a ROC such as this, the corresponding x(n) will be two-sided, i.e. non-causal.

## Slide 18: ROCs and poles and zeros
ROCs may be deduced from poles and zeros of X(z).
More than one ROC may be compatible with a particular set of poles and zeros.
Different ROCs correspond to different (impulse) response sequences x(n) with different causality and stability characteristics.
If ROC extends outwards to infinity then system is causal.
Since most physical systems, including the digital filters we will implement, are causal, we will be concerned mainly with such ROCs and with right-sided sequences (signals) starting at n=0 and for which the one-sided or unilateral z-transform may be used.
Notes: The same z-transfer function X(z) may correspond to a number of different impulse responses.
Huh? We are familiar with the concept that a linear time invariant system is described completely by its impulse response and in broad terms we understand the z-transfer function X(z) to be an equivalent/alternative system representation.
What we are seeing is that, strictly (correctly) speaking, a linear time invariant system is described completely by its z-transfer function (algebraic expression in z) and a region of convergence.

## Slide 19: ROC and the unit circle
causal and stable impulse response
Notes: Recall that if the ROC includes the unit circle then the corresponding sequence x(n) is stable. In the following three examples, causal or right-sided sequences are considered – these correspond to ROCs that extend outwards from a circle containing the outermost pole of X(z). Here the sequence x(n) is referred to as an impulse response, implying that X(z) is considered to be the z-transfer function of a system, and causality and stability properties are attributed to that system. In more general terms, X(n) and X(z) are simply signals.
Systems encountered in the physical world are casual – that includes systems (filters) implemented by us – and hence are of most interest.

## Slide 20: ROC and the unit circle
causal and unstable impulse response
Notes: In this case, the outermost pole of X(z) lies outside the unit circle and the causal system described is unstable.

## Slide 21: ROC and the unit circle
causal and unstable impulse response
Notes: In this case, the outermost pole of X(z) lies on the unit circle and the causal system described is unstable.
The conclusion that may be drawn from these three examples is that for right-sided x(n) all poles must lie inside (and not on) the unit circle for stability.

## Slide 22: Properties of the z-transform
Linearity
If
and
then

## Slide 23: Properties of the z-transform
Time Delay or Shift
If
then
Quantity z-m in the z-domain corresponds to a shift of m sampling instants in the time domain.
Notes: It was mentioned (much) earlier that the complex variable z may be considered as an operator representing a shift of one sample in a sequence.

## Slide 24: Properties of the z-transform
Convolution
The forced output y(n) of an LTI system having impulse response h(n) and input x(n) is given by the convolution sum
Taking the z-transform of this
Notes: Taking the z-transform of a convolution sum, and re-arranging it, takes a fair amount of algebraic manipulation (for a lecture slide) but yields a very important result.

## Slide 25: Properties of the z-transform
Changing the order of summation
Letting l = n-m

## Slide 26: Properties of the z-transform
In other words
The z-transform of the linear convolution of sequences h(n) and x(n) is equal to the product of their z-transforms H(z) and X(z).
Notes: This important result is often referred to by stating that ‘convolution in the time-domain is equivalent to multiplication in the z- ( or frequency-) domain’ and is well worth committing to memory.

## Slide 27: Properties of the z-transform
The convolution property leads to the concept of the z-transfer function where h(n) is the impulse response of a system.
Notes: A z-transfer function (the z-domain characterisation of a system) is the z-transform of a discrete impulse response (the time-domain characterisation of a system). Don’t forget that strictly the z-domain characterisation of a system comprises z-transfer function and ROC.

## Slide 28: Inverse z-transform
In theory, the inverse z-transform is found by contour integration but in practice usually found by partial fraction expansion and the use of z-transform tables.
z-transform tables should include ROCs
Notes: Here is a (very small) selection of z-transform pairs (examples that we have considered earlier) as they would appear in a table of z-transforms. The table is of particular use in finding inverse z-transforms, i.e. given X(z), what is x(n)? As discussed earlier, for the example X(z) = z/(z-a) different regions of convergence, corresponding to different forms of sequence x(n) are possible.