## Slide 1
Discrete-Time Fourier Transform
Notes: The discrete-time Fourier transform allows Fourier analysis of aperiodic discrete-time signals, that is the representation of aperiodic discrete-time signals in the frequency-domain.

## Slide 2: Discrete-Time Fourier Transform DTFT
How can we represent a discrete-time sequence in the frequency domain?
How do we apply Fourier analysis to sequence ?
Notes: What is the frequency domain representation of the sampled signal ?
And what is the nature of its frequency-domain representation?
So far we have looked at the Fourier analysis of continuous-time signals , whether periodic or aperiodic, using the Fourier series and the Fourier transform respectively.
is not a function of time but a sequence, or series, of numbers (discrete sample values).
If we replace, or represent, continuous-time signal 𝑥(𝑡) by samples of 𝑥(𝑡) taken at regular intervals in time 𝑡=𝑛𝑇, where 𝑛 is an integer index and 𝑇 is the sampling period in seconds we obtain a discrete time signal or sequence 𝑥(𝑛)=𝑥(𝑛𝑇) that is the 𝑛th value in the discrete-time sequence is equal to the continuous-time signal (sampled at) time 𝑡=𝑛𝑇. The values of 𝑥(𝑡) at times other than at the sampling instants are not represented explicitly in 𝑥(𝑛).
What is the frequency domain representation of the sampled signal 𝑥(𝑛)?
So far we have looked at the Fourier analysis of continuous-time signals, whether periodic or aperiodic, using the Fourier series and the Fourier transform. 𝑥(𝑛) is not a function of time but a sequence, or series, of numbers (discrete sample values).
One way of applying Fourier analysis to a discrete-time signal 𝑥(𝑛) is to represent it as a continuous–time signal 𝑥_𝑛 (𝑡) comprising a sum of weighted and time-shifted impulses as shown here, and then to apply the Fourier transform.
The result is a function of (continuous) frequency 𝑋(𝜔). 𝑋(𝜔) is periodic with period 𝜔=2𝜋∕𝑇 radians per second.

## Slide 3: Discrete-Time Fourier Transform DTFT
Continuous–time representation of discrete sequence
Fourier transform of
Notes: One way of applying Fourier analysis to a discrete-time signal is to represent it as a continuous–time signal comprising a sum of weighted and time-shifted impulses as shown here, and then to apply the (continuous-time) Fourier transform.
The th value in the discrete-time sequence is equal to the continuous-time signal (sampled) at time . The value of at times other than at the sampling instants is not represented explicitly in .
The result (of applying the DTFT) is a (continuous) function of frequency . is periodic with period radians per second.
One way of applying Fourier analysis to a discrete-time signal 𝑥(𝑛) is to represent it as a continuous–time signal 𝑥_𝑛 (𝑡) comprising a sum of weighted and time-shifted impulses as shown here, and then to apply the (continuous-time) Fourier transform.
If we replace, or represent, continuous-time signal 𝑥(𝑡) by samples of 𝑥(𝑡) taken at regular intervals in time 𝑡=𝑛𝑇, where 𝑛 is an integer index and 𝑇 is the sampling period in seconds we obtain a discrete time signal or sequence 𝑥(𝑛)=𝑥(𝑛𝑇).
The 𝑛th value in the discrete-time sequence is equal to the continuous-time signal (sampled at) time 𝑡=𝑛𝑇. The values of 𝑥(𝑡) at times other than at the sampling instants are not represented explicitly in 𝑥(𝑛).
The result is a function of (continuous) frequency 𝑋(𝜔). 𝑋(𝜔) is periodic with period 𝜔=2𝜋∕𝑇 radians per second.

## Slide 4: Discrete-Time Fourier Transform DTFT
We obtain the same result if we take the expression for the continuous
Fourier transform of and replace with.
DTFT of is equal to FT of
Notes: Another (arguably simpler) way of deriving the DTFT is simply to substitute for in an expression for the (continuous-time) Fourier transform of .
If we replace, or represent, continuous-time signal by samples of taken at regular intervals in time , where is an integer index and is the sampling period in seconds we obtain a discrete time signal or sequence .
Another way of deriving the DTFT is simply to substitute 𝑛𝑇 for 𝑡 in an expression for the (continuous-time) Fourier transform of 𝑥(𝑡).

## Slide 5: Discrete-Time Fourier Transform - Normalised Frequency
It is both convenient, and conventional to express the DTFT
as a function of normalised frequency
The units of are radians and is periodic with period radians.
Notes: What it says here.

## Slide 6: Discrete-Time Fourier Transform DTFT
Forward and inverse DTFT expressions
is periodic with period finding requires integration of
one cycle of .
The DTFT shares many properties with the Fourier transform, including
(but not limited to) linearity, duality, scaling and time and frequency shifting.
Notes: These two equations describe the forward (analysis) and inverse (synthesis) equations of the DTFT

## Slide 7: Discrete-Time Fourier Transform - Linearity
Linearity
If and
then
Notes: The discrete-time Fourier transform is linear. It obeys the law of superposition.
The discrete-time Fourier transform is linear. It obeys the law of superposition.
Shifting discrete-time sequence 𝑥(𝑛) by an integer number of sample positions 𝑛_0 in the time-domain corresponds to multiplying the DTFT of 𝑥(𝑛) , 𝑋(𝜔 ̂ ) by 𝑒^(−𝑗𝜔 ̂𝑛_0 ).
𝑒^(−𝑗𝜔 ̂𝑛_0 ) is a complex quantity with unity magnitude. Multiplying by 𝑒^(−𝑗𝜔 ̂𝑛_0 ) effects a linear phase shift.

## Slide 8: Discrete Time Fourier Transform DTFT – Time Shift
Time Shift
Start from the definition of the DTFT and change variable to variable
.
The DTFT of is given by
Notes: Shifting discrete-time sequence by an integer number of sample positions in the time-domain corresponds to multiplying the DTFT of , by .
is a complex quantity with unity magnitude. Multiplying by effects a linear phase shift.
Shifting discrete-time sequence 𝑥(𝑛) by an integer number of sample positions 𝑛_0 in the time-domain corresponds to multiplying the DTFT of 𝑥(𝑛) , 𝑋(𝜔 ̂ ) by 𝑒^(−𝑗𝜔 ̂𝑛_0 ).
𝑒^(−𝑗𝜔 ̂𝑛_0 ) is a complex quantity with unity magnitude. Multiplying by 𝑒^(−𝑗𝜔 ̂𝑛_0 ) effects a linear phase shift.

## Slide 9: Discrete Time Fourier Transform DTFT – Frequency Shift
Frequency Shift
The DTFT of is equal to the DTFT of using in place of .
Notes: Multiplying by in the time-domain results in a shift of in the frequency-domain.
Multiplying 𝑥(𝑛) by〖 𝑒〗^(−𝑗𝑛𝜔 ̂_0 ) in the time-domain results in a shift of 𝜔 ̂_0 in the frequency-domain.

## Slide 10: Discrete-Time Fourier Transform - Periodicity
Periodicity
Notes: The period of the DTFT in the frequency domain ( radians) corresponds to the sampling frequency of the discrete-time signal .
The period of the DTFT 𝑋(𝜔 ̂) in the frequency domain (2𝜋 radians) corresponds to the sampling frequency of the discrete-time signal 𝑥(𝑛).

## Slide 11: Discrete Time Fourier Transform - Duality
Forward and inverse DTFT expressions
Forward and inverse FS expressions
Notes: The discrete-time Fourier transform is the dual of the Fourier series. Substitute for , for , for , and for .
The discrete-time Fourier transform is the dual of the Fourier series. Substitute 𝑡 for −𝜔 ̂ , 𝑥(𝑡) for 𝑋(𝜔 ̂ ) , 𝑇 for 2𝜋 , and 𝑋(𝑘) for 𝑥(𝑛).

## Slide 12: Discrete Time Fourier Transform - Existence
The DTFT of exists/converges if, for any , .
Using the definition of the DTFT
That is is absolutely summable, which is satisfied if
must be absolutely summable for its DTFT to exist.
Notes: A valid function should be finite for any value of its independent variable.
For the DTFT to exist or converge, must be absolutely summable.
In other words, no value in the sequence may be infinite in magnitude and the sequence must either be finite in length or its values must decay towards zero as approaches plus or minus infinity.
The discrete-time Fourier transform is the dual of the Fourier series. Substitute 𝑡 for −𝜔 ̂ , 𝑥(𝑡) for 𝑋(𝜔 ̂ ) , 𝑇 for 2𝜋 , and 𝑋(𝑘) for 𝑥(𝑛).

## Slide 13: Discrete-Time Fourier Transform - Examples
DTFT of discrete-time impulse
DTFT exists, since dis absolutely summable
Notes: For the DTFT𝑋(𝜔 ̂ ) to exist or converge, 𝑥(𝑛)x(n) must be absolutely summable, that is the sum of all magnitudes of 𝑥(𝑛)x(n) must be finite. In un rigorous terms that means that 𝑥(𝑛)x(n) must be finite in extent (as well as finite in magnitude) or decays towards zero if it is infinite in extent.

## Slide 14: Discrete-Time Fourier Transform - Examples
DTFT of a finite length sequence
DTFT exists, since is absolutely summable
Notes: For the DTFT𝑋(𝜔 ̂ ) to exist or converge, 𝑥(𝑛) must be absolutely summable, that is the sum of all magnitudes of 𝑥(𝑛) must be finite. In un rigorous terms that means that 𝑥(𝑛)x(n) must be finite in extent (as well as finite in magnitude) or must decay towards zero if it is infinite in extent.

## Slide 15: Discrete-Time Fourier Transform - Examples
DTFT of an infinite length sequence
By inspection, is absolutely summable only for
Notes: The DTFT of an infinite length sequence is possible if the value of decays towards zero as tends to infinity.
The DTFT of an infinite length sequence 𝑥(𝑛) is possible if the value of 𝑥(𝑛) decays towards zero as 𝑛 tends to infinity.

## Slide 16: Discrete-Time Fourier Transform - Examples
DTFT of an infinite length sequence
By inspection, is absolutely summable only for
Notes: If the value of doesn’t decay towards zero as tends to infinity as, for example, in the case of a unit step function then the DTFT of doesn’t exist.
If the value of 𝑥(𝑛) doesn’t decay towards zero as 𝑛 tends to infinity as, for example, in the case of a unit step function then the DTFT of 𝑥(𝑛) doesn’t exist.

## Slide 17: Discrete-Time Fourier Transform - Examples
DTFT of an infinite length sequence
By inspection, is absolutely summable only for
Notes: The DTFT of this sequence doesn’t exist/converge.

## Slide 18: Discrete-Time Fourier Transform - Examples
These constraints on convergence are part of the Taylor series approximation
for
Notes: Even if the sequence is absolutely summable, if it’s infinite in length then the algebraic expression for its DTFT is infinite in length too. The Taylor series approximation for a power series can simplify the expression for the DTFT.
Even if the sequence 𝑥(𝑛) is absolutely summable, if it’s infinite in length then the algebraic expression for its DTFT is infinite in length too. The Taylor series approximation for a power series can simplify the expression for the DTFT.

## Slide 19: Discrete-Time Fourier Transform - Examples
Arguably, the DTFT of doesn’t exist since
You may see tables of DTFT pairs including
but the expression on the right is undefined for .
Strictly, the DTFT is not applicable to periodic functions.
Notes: Although tables of DTFT pairs may include the pair shown here, strictly the DTFT of a sinusoidal sequence doesn’t exist/converge.

## Slide 20: Discrete-Time Fourier Transform and FIR filters
The continuous frequency response of an FIR filter is given by the DTFT
of its coefficients (its impulse response).
Notes: A particularly useful application of the DTFT is that it maps between the impulse and frequency responses of an FIR filter.